## Slide 1: Buoyancy
Dr. Joel Cahoon
Civil Engineering
Summer 2009

## Slide 2
Buoyancy – Does an object float or sink?
Write on a piece of paper a list of things that might determine whether an object floats or sinks.

## Slide 3: Buoyancy
Does an object float or does it sink?
Civil engineering students have a contest to design and race a canoe made from concrete!
Montana State University
American Society of Civil Engineers

## Slide 4
Some concrete canoes float better than others!
University of Kansas – Daily Kansan
Photo by Anna Faltermeier

## Slide 5: What is a Force?
The weight of an object is a force.
We will work with forces using the units of “pounds”.
Pounds is abbreviated “lb”.

## Slide 6
Force
This concrete canoe weighs 330 pounds.
Miss St University Relations News Bureau
(662) 325-3442
Contact: Robbie Ward
June 11, 2007

## Slide 7: Forces
There are many ways to exert a force.
However, to determine buoyancy we only need to deal with the forces related to gravity.

## Slide 8: Gravitational Forces
195
pounds
Weight of Object,
w = 195 pounds
=
w
The box doesn’t look like a canoe, but representing the canoe as a box simplifies our drawings.

## Slide 9: What is a Force Balance?
Weight of Object,
w = 195 lb
=
w
Supporting Force,
Fe = 195 lb
+
w
The scale itself is providing the supporting force, and the supporting force is equal to the weight of the object.
w
Up is (+)
Down is (-)
Note:
195
lb
Fe

## Slide 10: Other Supporting Forces?
The supporting force is from above. There is no supporting force from below.
Supporting Force,
Fe = 150 lb

## Slide 11
Other Supporting Forces?
0 lb
Weight of Object,
w = 150 lb
=
w
Supporting Force,
Fe = 150 lb
+
Fe
w
The supporting force is from above, and since it is equal to the weight of the object, the scale provides no support.

## Slide 12: More Than 1 Supporting Force?
Crouch on a bathroom scale. Have two strong friends start to lift you by your elbows. Is there a point where half your weight is supported by your friends and half your weight is supported by the scale?
In the diagram, the block represents you.
0.5 w
Fe = 0.5 w
w

## Slide 13: Why is there a Force Balance?
Newton’s 2nd Law:
Sum of All Forces Acting on a Body = Mass x Acceleration
If the body is not accelerating (it is either stationary or moving at a constant velocity) then Acceleration equals zero. So, a body at rest has:
Sum of All Forces Acting on a Body = 0
Don’t forget signs (+, - )!

## Slide 14: Force Balance on a Submerged Object
Water Surface
Supporting Force, Fe
Buoyant Force, Fb
Weight of Object, w

## Slide 15: Force Balance on a Submerged Object
The buoyant force, Fb, is determined by Archimedes’ Principle:
The buoyant force equals the weight of the water displaced by the object.
Fb = g x Vd
g = the unit weight of the water (lb/ft3)
Vd = the volume of water occupied by the submerged portion of the object (ft3).

## Slide 16: What is the Unit Weight of Water?
A 1 foot cube of water weighs 62.4 lb. So, for water:
g = 62.4 lb/1 cubic foot = 62.4 lb/ft3
1 ft
1 ft
1 ft
=
62.4 lb
Water

## Slide 17: What is the volume displaced?
Water Surface
3 ft
3 ft
3 ft
Because this is a cube:
Vd = length x width x depth
Vd = 3 ft x 3 ft x 3 ft = 9 ft3
Depends on the shape. Here’s an example:

## Slide 18: What is the volume displaced?
Water Surface
6 ft
Because this is a cylinder:
Vd = p x (diameter/2)2 x length
Vd = 3.1416 x (3 ft/2)2 x 6 ft = 42.41 ft3
3 ft
Depends on the shape. Here’s an example:

## Slide 19: Now what, does it float or not?
Let’s say that an object is submerged in the water and then released. At the moment it is released, there is nothing holding it up from above and it is not resting on a solid object below. That’s the same as saying the supporting force, Fe, is zero.
Fe = 0
Fb
w
Fb
w
=

## Slide 20: Now what, does it float or not?
At the moment of release there are only two forces left (w and Fb). With only two forces, there are only three possible cases:
Fb
w
w is greater than Fb (w > Fb)
w is less than Fb (w < Fb)
w is equal to Fb (w = Fb)

## Slide 21: Case 1
w is greater than Fb (w > Fb)
Fb
w
If w is greater than Fb, then the sum of the forces is (w points downward, so w is negative):
sum of forces = (-w) + Fb
which will be a negative number!
Side Note:
Notice the length of the arrows.

## Slide 22: Case 1
w is greater than Fb (w > Fb)
Fb
w
If the sum of forces is non-zero, then the object is accelerating. Since the sum of forces is negative, the object is accelerating downward.
The object is sinking!

## Slide 23: Case 2
Fb
w
Since the sum of forces is positive, the object is accelerating upward.
The object is floating!
2. w is less than Fb (w < Fb)

## Slide 24: Case 3
Fb
w
Since the sum of forces is zero, the object is not moving at all (no acceleration).
The object is “neutrally buoyant”. It just stays in the place where it was released!
3. w equals Fb (w = Fb)

## Slide 25: An example
A brick is 6 inches long, 3 inches wide and 3 inches tall. The brick was placed on a scale and weighed 4 lb. When submerged and then released, will the brick float?
4 lb
6 in
3 in
3 in
The weight of the object, w, is 4 lb.
w = 4 lb

## Slide 26: An example
A brick is 6 inches long, 3 inches wide and 3 inches tall. The brick was placed on a scale and weighed 4 lb. When submerged and then released, will the brick float?
6 in
3 in
3 in
Vd = (6 in x 1 ft/12 in) x (3 in x 1 ft/12 in) x (3 in x 1 ft/12 in)
Vd = (0.5 ft) x (0.25 ft) x (0.25 ft)
Vd = 0.03125 ft3
What is the volume displaced, Vd?

## Slide 27: An example
A brick is 6 inches long, 3 inches wide and 3 inches tall. The brick was placed on a scale and weighed 4 lb. When submerged and then released, will the brick float?
6 in
3 in
3 in
Fb = g x Vd
Fb = 62.4 lb/ft3 x 0.03125 ft3 = 1.95 lb
What is the buoyant force, Fb?

## Slide 28: An example
A brick is 6 inches long, 3 inches wide and 3 inches tall. The brick was placed on a scale and weighed 4 lb. When submerged and then released, will the brick float?
What is the sum of the forces?
Sum of forces = (-4 lb) + 1.95 = -2.05 lb
Sum of forces is negative, so the brick will accelerate downward. The brick will sink!
Fb = 1.95 lb
w = 4 lb

## Slide 29: Another example
A block of wood is 6 inches long, 3 inches wide and 3 inches tall. The block was placed on a scale and weighed 1 lb. When submerged and then released, will the block float?
1 lb
6 in
3 in
3 in
The weight of the object, w, is 1 lb.
w = 1 lb

## Slide 30: Another example
6 in
3 in
3 in
Vd = (6 in x 1 ft/12 in) x (3 in x 1 ft/12 in) x (3 in x 1 ft/12 in)
Vd = (0.5 ft) x (0.25 ft) x (0.25 ft)
Vd = 0.03125 ft3 Same as the brick!
What is the volume displaced, Vd?
A block of wood is 6 inches long, 3 inches wide and 3 inches tall. The block was placed on a scale and weighed 1 lb. When submerged and then released, will the block float?

## Slide 31: Another example
6 in
3 in
3 in
Fb = g x Vd
Fb = 62.4 lb/ft3 x 0.03125 ft3 = 1.95 lb Same as the brick!
What is the buoyant force, Fb?
A block of wood is 6 inches long, 3 inches wide and 3 inches tall. The block was placed on a scale and weighed 1 lb. When submerged and then released, will the block float?

## Slide 32: Another example
What is the sum of the forces?
Sum of forces = (-1 lb) + 1.95 = 0.95 lb
Sum of forces is positive, so the brick will accelerate upward. The wood block will float!
Fb = 1.95 lb
w = 4 lb
A block of wood is 6 inches long, 3 inches wide and 3 inches tall. The block was placed on a scale and weighed 1 lb. When submerged and then released, will the block float?

## Slide 33: A third example
A block of wood is 6 inches long, 3 inches wide and 3 inches tall. The block was placed on a scale and weighed 1 lb. When submerged and then released, we have shown the block will float. Now, how much of the block will be above water?
Water Surface
Like this?
Or like this?

## Slide 34: A third example
From the second example:
Vd = 0.03125 ft3
But this was based on the whole block being under water. Now it is only partially submerged. The submerged volume is still (length x width x depth), but now the depth is only the portion under water:
depth

## Slide 35: A third example
Once the block of wood floats to the top and comes to rest, it is no longer accelerating. If it is not accelerating, then the sum of forces equals zero. So we can solve Newton’s 2nd law for the unknown submerged depth.
Sum of forces = (-w) + Fb = 0
0 = (-w) + Fb
0 = (-w) + g x Vd
0 = (-w) + g x (6 in x 1 ft/12 in) x (3 in x 1 ft/12 in) x (depth)
Fb = 1 lb
w = 1 lb

## Slide 36: A third example
Substitute values for w and g, rearrange the equation and solving for the depth:
Fb = 1 lb
w = 1 lb
w = g x (6 in x 1 ft/12 in) x (3 in x 1 ft/12 in) x (depth)
1 lb = (62.4 lb/ft3) x (6 in x 1 ft/12 in) x (3 in x 1 ft/12 in) x (depth)
depth =
1 lb
(62.4 lb/ft3) x (6 in x 1 ft/12 in) x (3 in x 1 ft/12 in)
= 0.128 ft
depth = 0.128 ft x (12 in/1 ft) = 1.54 inches

## Slide 37: A third example
So, 1.54 inches will be submerged, and the remaining 1.46 inches will be above the water.
Fb = 1 lb
w = 1 lb
Water Surface
1.54 in
1.46 in